MECH 4310 Analysis of Composite and Multifunctional Materials

HOMEWORK #2

Due Tuesday February 5th at 10:00

- For the following displacement field determine the strain fields (all 6 strain components) using Lagrangian infinitesimal strain theory.

- Determine whether compatibility is satisfied for the strain field you obtained for problem 1. (The compatibility equations are the solution to the last problem of HW#1)

- Given a cylinder of rubber that has a diameter of 20cm and a height of 20cm. If E=1.0GPa and =0.3, plot the applied compressive load as a function of axial deformation a) assuming small displacements and infinitesimal strain theory and b) assuming large displacements/deformations. But both curves on the same plot and discuss the differences. Suggestion for part b) set-up an equation in excel or other software to do the calculations using an incremental approach.

- Repeat problem 4 but now with a tensile load.

- Repeat part 4 b) but with =0.5 and compare this result to the result for 4b)